## Slide 1: Unmanned Maritime Autonomy Architecture
DISTRIBUTION A. Approved for public release: distribution unlimited
Distribution Statement A
Distribution Statement A

## Slide 2: What is UMAA?
UMAA’s goal is to “realize” a shared services approach:
Enable software reuse across programs and platforms
Provide government-owned interface definitions to enable software interoperability
Enable the development of best-of-breed software components with standard interfaces
Enable industry contribution at a software component level versus only at a system level
UMAA defines interfaces for common autonomy services for unmanned surface and undersea vehicles
UMAA enables the development of “software services” akin to software “libraries”
UMAA enables the reuse of software services across programs that are developed as UMAA compliant
UMAA specifies protocols leveraging the “Data Distribution Services” (DDS) Standard and expanding to enable interoperability
UMAA is NOT “plug and play” - system engineering beyond the scope of UMAA is required for full interoperability of UMAA services
UMAA does NOT implement or provide software (except for examples, i.e., reference implementations)
A PMS 406 initiative to standardize interfaces to enable interoperability of system software for all USV and UUV programs

## Slide 3: Systems of Today
Vehicles
Payloads
External C2
TOPSIDE
MOCU
CCS
Other
Mission
Autonomy
Vehicle Interfaces
Unique
Vehicle
I/Fs
Payload Interfaces
Unique
Payload
I/Fs
C2 Interfaces
Unique C2 Interfaces
Veh1..n x Payld1..m x C21…r
Currently develop a specific solution for each:
vehicle – mission – payload – C2 combination
(pick one of each)
Motivation behind UMAA

## Slide 4: Interface Standards Approach
Vehicles
Payloads
External C2
Common C2
Mission
Autonomy
Standard Services and Interfaces
Make Systems Comply to a Standard
Interface Standards
Interface Standards
Reduce scope
Reduce cost
Map/Chart Services
Navigation Services
Data Fusion Services
Communication Services
Other Services….
Mission
Autonomy
Vehicles – interface content vastly common across vehicles
Payloads - Varies by type so exploit commonality by type
Interface Standards
Motivation behind UMAA

## Slide 5: Shared Services Approach
Mission Autonomy
Maneuver Operations
Engineering Operations
Situational Awareness
Sensor/Effector Management
Mission Management
Communication Operations
Waypoint Status
DDS Bus
DDS Bus
Ownship Position
Waypoint Control
Mission Plan
Engine Status
Fuel Status
Battery Status
Mission Control
Mission Status
Waterspace Plan
Ownship Velocity
Ownship Acceleration
Contact
Comms Status
Comms Control
CTD
Waterspace
Compartment Status
Sea State
Time
Engine Control
Anchor Status
Anchor Control
Propulsor Status
Propulsor Control
Rudder Status
Rudder Control
Thruster Status
Thruster Control
Light Status
Light Control
Bell/Whistle/Gong Status
Bell/Whistle/Gong Control
Vector Status
Vector Control
Hover Status
Hover Control
Drift Status
Drift Control
Racetrack Status
Racetrack Control
Stationkeep Status
Stationkeep Control
GPS Status
INS Status
Camera Specifications
PTU Status
Still Image
Camera Configuration
PTU Control
Digital Video Specifications
Digital Video Configuration
H264 Specifications
H264 Configuration
Vehicle and Payload Systems
Autonomy
Engine 3
Mission Autonomy
Autonomy
Engine 2
Mission Autonomy
Autonomy
Engine 1
Motivation behind UMAA
Green shows notional services available on a shared DDS bus

## Slide 6
Standardizing common control and standardizing autonomy services provides an extensible solution for operators and developers to engage with increasing autonomy capabilities
Common Control System (CCS) is a separate initiative from UMAA to establish the operator control system
UMAA scope is confined to the onboard capabilities in a vehicle including the ability to collaborate autonomously with other vehicles
UMAA Scope

## Slide 7
Specification
Working Group (SWG)
- Members*
SME Consultants*
Program Manager*
CAPT Searles
CDR Delwiche
Reference Implementation Working Group (RWG)
- Implementation Lead(s)*
Program Development
(LDUUV, XLUUV, Razorback, MUSV, LUSV,…)
PM Liaison
Representative for Platform*
Industry
Unmanned Maritime Autonomy Architecture Board (UMAAB*)
Chair*
Members*
- Program office coordination
- Architecture definition and evolution
- Governance
- Compliance standard
- Configuration control (IDL, ICDs, Reference Implementation
- Weekly teleconferences
- Industry days (live and virtual)
- Model updates
- ICD content
- ICD/IDL tool chain
- Weekly teleconferences
- Reference Implementation
- Portability testing
- Compliance testing
- Bi-weekly teleconferences
Liaison with UMAAB
Advocate for program requirements
Unmanned Maritime Autonomy Architecture
(UMAA) Interface Control
Working Group (ICWG)
(Direction, coordination)
* Formal names from UMAAB charter
(Recommended updates)
- Direction
- Membership
- Approval of deliverables
- Cross program coordination
(Direction, coordination)
(Program requirements)
(ICDs, IDL, Compliance)
- Interface input / feedback
- UMAA implementations
UMAA Organization
(Update requests)
(ICDs, IDL,
Compliance)

## Slide 8: Unmanned System Standards
Joint Architecture for Unmanned Ground Systems (JAUGS)
  OSD charter established JAUGS WG 1997
  OSD updated charter established JAUS WG 2002
  JAUS governance transitioned to SAE AS-4 Committee 2004
  Original stakeholders – Ground robotics
UAS (Unmanned Aircraft Systems) Control Segment (UCS) Architecture
  OSD charter established UCS WG 2009
  UCS governance transitioned to SAE AS-4 Committee 2015
  SAE charter updated UxS Control Segment (UCS) 2015
  Stakeholders
    Common Control System (CCS)
UCSMDE (Multi-Domain Extension)
  OSD promoted UCS for the maritime domain 2013
  Evolved over the next few years by Community of Interest (COI)
The Object Management Group (OMG) Data-Distribution Service for Real-Time Systems (DDS) used is an open international middleware standard using publish-subscribe communications for real-time and embedded systems.

## Slide 9: Alignment of UMAA and CCS
CCS
UMAA
UCS
(Version 3.4)
MDE
(JSON)
UxSDK
Tool
UCSMDE
UMAA
(FreeMarker
templates)
UxSDK
Tool
UMAA
ICD
UMAA
IDL
SAE AS-4UCS
Platform
Independent
Model (PIM)
Platform
Specific
Model (PSM)
UMAA and CCS under one version of the UCSMDE model with path for alignment with latest UCS standard

## Slide 10: UMAA Products
UMAA
Product Hierarchy
Governing Documents
Models
Interface Definition
Models
Reference
Implementations
Reference
Implementations
Reference
Implementations
Posted on Distro D website for industry access*
Formalized as NAVSEA Technical Publication T0300-BE-IDS-010
Published for government and industry partners as the basis for testing and verification
Published Feb 2019, released as Distro A in March 2020
Formal releases published at regular intervals, developmental releases published continuously (DevOps pipeline)
Used internally by UMAA team, available to programs as needed
Posted as available
* Originally hosted on Defense Intelligence Information Enterprise (DI2E), now transitioning to Naval LIFT
Architecture
Design
Description
Compliance
Specification
Governance
DevOps
Pipeline
Tools
Service
Specifications
Data
Models
Interface Control
Document (ICD) / Interface Definition Language (IDL)
Interface Control
Document (ICD) / Interface Definition Language (IDL)
…

## Slide 11: UMAA Interface Control Documents
services
services
services
services
services
services
Interface Control Documents (ICDs) – contain the definition for services that are building blocks for autonomy
ICDs will be extended over time – interfaces used in contractor-built services may be adopted into UMAA
This is a service interface example comprised of multiple attributes
ICDs are “buckets” that contain groups of logically related service interface definitions
VelocityControlCommand
Mission Management
(MM)
Situational Awareness
(SA)
Sensor and Effector Management (SEM)
Maneuver Operations
(MO)
Engineering Operations
(EO)
Support
Operations
(SO)
Processing Operations
(PO)
Communications Operations
(CO)

## Slide 12: Release of ICDs and IDL
UMAA RWG*
UMAA SWG*
UMAA
Board
Daily updates - Distro D
Developmental ICDs
Industry SME’s
Reference Implementation Teams
Program requests
*Specification Working Group (SWG), Reference Implementation Working Group (RWG)
JIRA
Issues
JIRA
Issues
JIRA
Issues
Optionally prototype
JIRA
Issues
JIRA
Issues
JIRA
Issues
Document
feedback
JIRA
Issues
JIRA
Issues
JIRA
Issues
Document
feedback
JIRA
Issues
JIRA
Issues
JIRA
Issues
Document
feedback
Result
ICDs/IDL
Four-month cycle
Release ICDs
Four-month cycle – Distro D
(Feb 2021, June 2021, Oct 2021)
Recommend for R&D and Prototyping
(updates rarely back out…)
Specified on Contracts
ICDs/IDL
Prioritize,
Assess,
Approve
Implement ICD/IDL
PMS 406
PM Review
NAVSEA Public Release Review
Final
Signoff
PMS 406
Technical
Review
Result
ICDs/IDL
Disto A
Release ICDs
Distro D to Distro A
(Review Dependent Dates)
Specified on Contracts
Useable for industry products
Four
Month
Cycle
?
Ongoing…
Distro A will lag Distro D
Goal is to compress this cycle
DISTRO A
Release Cycle

## Slide 13: Industry Participation
Regularly scheduled industry forums (physical and virtual) – (275)
Open participation model
  Direct industry involvement through standard industry tools
  Atlassian tool set on Naval LIFT (Confluence, JIRA, Bitbucket)
  Industry can submit updated requests
  Industry can monitor evolution of UMAA standards via JIRA used by the UMAA board to specify updates and changes
  Continuous posting of updated developmental products
Reference Implementation Working Group (RWG)
  Ongoing example code responding to industry input to help boot-strap industry implementations, e.g., UMAA (How-To's) in Bitbucket
  Three RWG teams using UMAA ICD/IDL outputs

## Slide 14: Process Workflow

## Slide 15: UMAA Today
Released v5.2.1 April 20, 2022
Moving to a more controlled process
  High-bar for breaking changes, requiring PMS 406 approval
  Improved vetting and prototyping for new services
Transition from DI2E to Naval LIFT
Collaboration with PMS 406 Autonomy Framework Working Group (AFWG) to group services into components
Next Industry Day tentatively late Fall 2022